## Slide 1: FPGA Design Challenge :Techkriti’14 Digital Design using Verilog – Part 2
Anurag Dwivedi

## Slide 2: Recap
Verilog- Hardware Description Language
Modules
Combinational circuits
assign statement
Control statements
Sequential circuits
always@ block
Blocking and non-blocking statements

## Slide 3: Modular Circuits
Time to construct larger modules from smaller modules.
Various modules are interconnected to make a larger circuit (or module).
Each sub-module has a separate Verilog file.
A sub-module may have another sub-module in its circuit.
One needs to indicate the top level module before synthesis.

## Slide 4: Example
Sub-module 1
module Sub1 (input wire [7:0] a1, output wire [7:0] b1);
Sub-module 2
module Sub2 (input wire [7:0] a2, output wire[7:0] b2);
Top Module
Module Top (input wire [7:0] a, output wire[7:0] b);

## Slide 5: Instantiation
Used to create instances of the module and create connections among different modules.
In the above example, we need to instantiate the two sub-level modules in the top module.
This is done as follows:
wire [7:0] c;
Sub1 Encoder (.a1(a), .b1(c));
Sub2 Decoder (.a2(c), .b2(b));

## Slide 6: Example : Full Adder
module FAdder(
input wire [3:0] A, B,
output wire cout,
output wire [3:0] S );
wire c0, c1, c2;
FA fa0( .a(A[0]), .b(B[0]), .cin(0),.cout(c0), .sum(S[0]));
FA fa1( .a(A[1]), .b(B[1]), .cin(c0), .cout(c1), .sum(S[1]));
FA fa2( .a(A[2]), .b(B[2]), .cin(c1), .cout(c2), .sum(S[2]));
FA fa3( .a(A[3]), .b(B[3]), .cin(c2), .cout(cout), .sum(S[3]));
endmodule

## Slide 7: Points to note
All output ports of instantiated sub-module should be of wire data-type.
Note in previous example, c0,c1,c2 and S are wires.
Inputs may be reg or wire.
Suppose in above, [3:0] S was of reg type.
  Declare a dummy wire variable [3:0] add
  Pass add[0], add[1] … to the instantiations
  Finally put:
    always@(*)
    S <= add;

## Slide 8: Parameterized Modules
A generalized type of module.
Can be instantiated to any value of parameter.
Parameterization is a good practice for reusable modules
Useful in large circuits.

## Slide 9: N-Bit adder
module AdderN #(parameter N = 4)(
input wire [N-1:0] IN1,
input wire [N-1:0] IN2,
output reg [N-1:0] OUT );
always @(*)
OUT <= IN1 + IN2;
endmodule

## Slide 10: Instantiation of Parameterized Modules
<Module Name> #(.<Parameter Name>(value)) <Instance name>
( .IN1(…) , .IN2(…), .OUT1(…), .OUT2(…) );
Example :
AdderN # ( .N(16) ) Add16 ( .IN1(in1), .IN2(in2), .OUT(out) );

## Slide 11: Test Bench
Used to test the functionality of design by simulation.
Instantiate our top most module and give varying inputs & verify if the outputs match expected results.
Added functionalities in Test Bench:
  Delays
  $display(), $monitor()

## Slide 12: Delays
Not synthesized
Can be used to model delays in actual circuit during simulation
Used mostly in Test Benches to provide inputs at particular instants.
Syntax: #<time steps>
  #10 q = x + y; // inter assignment delay
  q = #10 x + y; // intra assignment delay
  Most common:
  always
#5 clk = ~clk;

## Slide 13: More features
$display()
  used for printing text or variables to screen
  syntax is the same as for printf in C
  $display("time, \tclk, \tenable, \tcount");
$monitor()
  keeps track of changes to the variables in the list
  whenever any of them changes, it prints all the values
  only written once in initial block.
  $monitor("%d,\t%b,\t%b,\t%b,\t%d",$time, clk, enable,count);
$finish
  Terminating simulation

## Slide 14: Test Bench Counter
module counter_tb;
reg clk, reset, enable;
wire [3:0] count;
counter C0( .clk (clk), .reset (reset), .enable (enable), .count (count) );
initial begin
clk = 0;
reset = 0;
enable = 0;
end
always
#5 clk = !clk;
initial begin
$display("time,\tclk,\tenable,\tcount");
$monitor("%d,\t%b,\t%b,\t%d",$time, clk,enable,count);
end
initial
#100 $finish;
endmodule

## Slide 15: Demonstration
4029 Counter
4-bit Full Adder

## Slide 16: FPGA Design Challenge Techkriti’14
Problem Statement :
The challenge in FPGA is to design and efficiently implement the Hilbert transformation of any given function.
It maps a time domain function to another time domain function by a convolution of the input signal with the function H(t) whose representation in frequency domain is:
Frequency domain representation of Hilbert Transform

## Slide 17: Fourier Transform
FT is a mathematical transformation to transform a signal from time domain to frequency domain.

## Slide 18: Basic Theory
If x(t) is our signal and h(t) is the signal corresponding to Hilbert Transform, then the Hilbert transform of x(t), hx(t) = x(t)*h(t)
FT(hx(t)) = FT(x(t)*h(t)) = X(f) x H(f)
Here, X(f) is the Fourier transform of x(t) and H(f) is the Fourier Transform of h(t) given by
hx(t) = IFT( X(f) x H(f) )

## Slide 19: Basic Theory
Find Fourier Transform of the function.
Multiply the FT by H(f)
Apply inverse Fourier Transform of the function obtained.

## Slide 20: Discrete Fourier Transform
How to model continuous time signals in our digital hardware?
  Work with samples of signal
  xi[n] = x (nT) ; n = 0,1 … N-1
  T is the sampling period
How to take Fourier transform?
  Take Discrete Fourier Transform

## Slide 21: DFT Matrix
Total number of operations : O(N^2)

## Slide 22: Fast Fourier Transform
Computation of DFT involves a lot of redundant operations
Time complexity can be reduced drastically by using this information
A class of algorithms known as Fast Fourier Transform (FFT) is developed for the same

## Slide 23: Cooley–Tukey algorithm : Radix 2 case
When N is a factor of 2
We have
Writing the odd and even numbered terms separately
Taking out the common factor

## Slide 24: Cooley–Tukey algorithm : Radix 2 case
Because of Periodicity of DFT we have
Finally,

## Slide 26: Further reduction in computation

## Slide 27: Complete Structure
O(N log(N))

## Slide 28: Basic Theory
To implement Hilbert transform in Verilog
  Find FFT of sequence
  Multiply it by –j sgn(k)
  Take IFFT of the resulting sequence

## Slide 29: Note
The approach mentioned above is one of the many possible solutions to the problem statement.
You should search more and look for better solutions.

## Slide 30: Judging criteria
Area (#LUTs, #FFs, #BRAMs, #DSP Elements etc.)
Latency (No. of cycles Reqd).
Need for external memory (eg. DRAM Controller – DDR/DDR2 and size of memory required).
Maximum frequency achieved.
Power consumption as reported by ISE tool.
Extra Feature : Implementation of a feature where Hilbert transform is being used